## Slide 1: University of Gujrat Department of Computer Science
Course Code : CS-252
Computer Organization and Assembly Language
Lecture #5
Registers - Flags

## Slide 2: Flags Register
A special register with individual bit positions that indicate the status of the microprocessor.

## Slide 3: Flags Register
CF = Carry Flag SF = Sign Flag
PF = Parity Flag TF = Trap Flag
AF = Auxiliary Carry Flag IF = Interrupt Flag
ZF = Zero Flag DF = Direction Flag
OF = Overflow Flag
-
-
-
-
OF
DF
IF
TF
SF
ZF
-
AF
-
PF
-
CF
0
15

## Slide 4: Status Flags
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
+ 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
16 – bit Accumulator
Carry Flag = CF
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
1
Carry Flag (CF)
Set if the result of an unsigned operation is too big to fit into the destination. 1 = carry, 0 = no carry.

## Slide 5: Status Flags
0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0
Overflow flag = OF
1
Result of addition of 2 positive numbers cannot be negative!
Overflow Flag (OF)
Set if the result of a signed operation is too wide to fit into the destination. 1 = overflow, 0 = no overflow.
+

## Slide 6: Status Flags
0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1
+ 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0
0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1
Auxiliary Carry Flag = AF
1 1 1
Carry out from bit 3 on addition
1
Auxiliary Carry Flag (AF)
Set when an operation causes a carry from bit 3 to bit 4 or a borrow from bit 4 to bit 3. 1= carry, 0 = no carry.

## Slide 7: Status Flags
Zero Flag (ZF)
Set when the result of an arithmetic operation is zero. 1 = zero, 0 = not zero.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Result
Zero Flag =ZF
1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0

## Slide 8: Status Flags
Parity Flag (PF)
If lower byte of the result contains even number of 1’s, the Parity Flag is set and for odd number of 1’s, the Parity Flag is reset.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
Result
Parity Flag = PF
1
0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0

## Slide 9: Status Flags
Sign flag (SF)
Set when the result of an operation is negative. 1 = negative, 0 = positive.
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
Sign Flag =SF
1
0
0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
MSB = 1
Negative
MSB = 0
Positive

## Slide 10: Control Flags
Direction flag (DF)
Used in string operation. If it is set, bytes are accessed from higher memory address to lower memory address. When it is reset, bytes are accessed from lower memory address to higher memory address.
Interrupt flag (IF)
Indicates if system interrupts can occur. Interrupts will be disabled if a critical operation is being performed that can not be interrupted.
Trap flag (TF)
Determines if the CPU is halted after each instruction. If it’s set, a debugger will allow single stepping through the program.