## Slide 1: University of Gujrat Department of Computer Science
Course Code : CS-252
Computer Organization and Assembly Language
Lecture # 7
Few instructions of Assembly Language

## Slide 2
Instruction Groups
Data Movement Instructions
Arithmetic / Logic Instructions
Program Control Instructions
Special Instructions

## Slide 3: Data Movement
mov ax,bx ; move data from bx to ax
lda 0234 ; load 0234 into ; accumulator

## Slide 4
and ax,1234 ; AND 1234 with ax
add bx,0534 ; ADD 0534 to bx
add bx,[1200] ; ADD data at address 1200 to bx
add ax,[1234] ; ADD data from address 1234 to ax
Arithmetic and Logic Instructions

## Slide 5
cmp ax, 0 ; compare ax with 0
jne 1234 ; jump if not equal to the instruction at ; address 1234
Program Control Instructions

## Slide 6
cli ; clear the interrupt flag
sti ; set the interrupt flag
Special Instructions

## Slide 7: Few Basic Instructions

## Slide 8: MOV instruction
Used to transfer data between registers, between a register and a memory location, or to move a number directly into a register
Syntax MOV destination, source
e.g. MOV AX, WORD1
MOV AX, BX
MOV AH, ‘A’

## Slide 9: Legal Combinations of Operands for MOV
Source Operand | Destination Operand |  |  | 
 | General Register | Segment Register | Memory Location | Constant
General Register | Yes | Yes | Yes | No
Segment Register | Yes | No | Yes | No
Memory Location | Yes | Yes | No | No
Constant | Yes | No | Yes | No

## Slide 10: XCHG instruction
Used to exchange the contents of two registers, or a register , or a register or a memory location
Syntax XCHG destination, source
e.g. XCHG AH, BL
XCHG AX, WORD1

## Slide 11: Legal Combinations of Operands for XCHG
Source Operand | Destination Operand | 
 | General Register | Memory Location
General Register | Yes | Yes
Memory Location | Yes | No

## Slide 12: ADD and SUB instructions
Used to add or subtract the contents of two registers, a register and a memory location and to add (subtract) a number to (from) a register or a memory location
Syntax ADD destination, source
SUB destination, source
e.g. ADD AH, BL
SUB AX, WORD1

## Slide 13: Legal Combinations of Operands for ADD and SUB
Source Operand | Destination Operand | 
 | General Register | Memory Location
General Register | Yes | Yes
Memory Location | Yes | No
Constant | Yes | Yes

## Slide 14: INC and DEC instructions
INC is used to add 1 to the contents of a memory location or register and DEC is used to subtract 1 from the contents of a memory location or register
Syntax INC destination
DE C destination
e.g. INC AX
DEC WORD1

## Slide 15: NEG instruction
NEG is used to negate the contents of the destination. NEG does this by replacing the contents by its 2’s complement
Syntax NEG destination
e.g. NEG AX